## Slide 1: Revolutionary War Weaponry
By Alex
http://www.11thpa.org/neumann.html

## Slide 2: 1: Early Assembled Fowler/Musket c.1740
Length: 671⁄4" Lock: 63⁄4"x13⁄8" Butt Tang: 27⁄8" Furniture: Brass/Iron Barrel: 511⁄8", .71 cal. Trigger Guard: 85⁄8" Sideplate: 41⁄8" Weight: 7.8 lbs.
This American firearm, which predates the War for Independence, illustrates the Colonists’ early reliance upon reused mixed parts. Jacob Man of Wrentham, Massachusetts , would later carry it as a Minuteman at Lexington/Concord and while a soldier in the 13th Massachusetts Continental Regiment through the New York-Trenton-Princeton campaigns (1775-1777), as well as at the Battle of Rhode Island (1778). The American stock mounts a bulbous Dutch lock, a convex French S-shaped iron sideplate, a cut-down British brass buttplate, an English trade pattern escutcheon and a crude locally cast brass trigger guard secured by four nails. A French pinned fowler barrel is stocked to the muzzle, indicating the early lack of socket bayonets. Its iron ramrod is held by three thimbles, of which the bottom one is an old Queen Anne ribbed pattern, and the others simple rolled sheet brass.
http://www.11thpa.org/neumann.html

## Slide 3: 2: A Club Butt Country Fowler c. 1715-1750
Although technically a hunting gun with the fore-end of its maple stock reaching to the muzzle of a European barrel, this family fowler, which omits all but the basic components, is typical of many of the existing arms carried into the field by the American forces early in the Revolution and by the militia throughout the war. Its stock is the popular civilian club butt form, but the non-essential buttplate, escutcheon, sideplate, raised carving and bottom ramrod pipe are not included. The Queen Anne period, three-screw flat lock design with its reinforced butt has an unbalanced profile which suggests possible Colonist manufacture. An uneven, hand-forged iron trigger guard, however, is obviously American-made. The wooden rammer is secured in two upper, sheet-brass thimbles.
Length: 60" Lock: 7"x11⁄8" Furniture: Brass/Iron Barrel: 45", .70 cal. Trigger Guard: 71⁄8" Weight: 7.5 lbs
http://www.11thpa.org/neumann.html
http://www.doublegv.com/ggv/battles/tactics.html

## Slide 4: 3: Early French Components c. 1760-1780
A French Model 1717 musket furnished most of the elements remounted on this American cherry stock. It might have been an arm captured during the Colonial Wars with French Canada, or an early arm among the foreign aid shipments during our Revolution. Included is the distinctive M. 1717 lock with its vertical bridle, a typical French flat S-shaped sideplate, a double-pointed trigger guard, a long butt tang, and a 47" barrel. The double-strap upper barrel band from a French Model 1754 musket had a cone-shaped ramrod pipe brazed to the bottom by the Colonists who were probably influenced by similar Spanish and Dutch designs. The provincial restocker also provided a New England petal-type raised carving around the barrel tang.
Length: 63" Lock: 61⁄2"x13⁄8" Butt Tang: 43⁄4" Furniture: Iron Barrel: 47", .70 cal. Trigger Guard: 125⁄8" Sideplate: 43⁄8" Weight: 9.2 lbs.
http://www.11thpa.org/neumann.html

## Slide 5: 4: British Brown Bess Elements c. 1775-1783
Major parts from a British Long Land 1756 Pattern musket, which was still the primary arm of their infantry early in the Revolution, were remounted by the rebels on a maple stock to create this firearm. In doing so, they reused the lock, trigger guard, sideplate, and buttplate, but omitted the original escutcheon, fourth rammer pipe and raised beavertail carving surrounding the barrel tang. The lock area of the stock, in turn, was made thicker by the Colonists, probably to strengthen that most vulnerable location from fractures. The convex side plate is also inset deeper than normal. An American hand-forged iron ramrod includes a thick button head, while the original 46" Brown Bess barrel has been shortened by 5⁄8" reflecting the constant need to dress the muzzle walls as they became sharpened from prolonged rammer wear.
Length: 60 5⁄8” Lock: 7”x1 1⁄4” Butt Tang: 53⁄4" Furniture: Brass Barrel: 453⁄8”, .77 cal. Trigger Guard: 11" Sideplate: 61⁄8" Weight: 10.3 lbs.
http://www.11thpa.org/neumann.html
http://www.doublegv.com/ggv/battles/tactics.html

## Slide 6: Other Muskets
http://www.11thpa.org/neumann.html

## Slide 7: British Musket Flintlocks
http://www.11thpa.org/neumann.html

## Slide 8: Credits
http://www.11thpa.org/neumann.html
http://www.doublegv.com/ggv/battles/tactics.htm
A Soldiers Life by Andrew Robertshaw